## Slide 1: 555 Timer

## Slide 2: Internal Block diagram

## Slide 4: Inside the 555 Timer
S | R | Q | Q
0 | 0 | No Change | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | X | X
Threshold
Control Voltage
Trigger
Discharge
Vref
+
R
S
Q
Q
Truth Table
Fig: Functional Diagram of 555 Timer
-

## Slide 6
The 555 Timer is one of the best known IC’s.
  The 555 is part of every experimenter's tool kit
  Capable of creating a wide variety of circuits, including:
    Oscillators with adjustable frequency and Duty Cycle
    Monostable Multivibrators
    Analog to digital Converters
    Frequency Meters
    Many other applications….
  The clock on the Vulcan Board is generated by a 555 timer.

## Slide 7: 555 Timer Configurations
In this course we will use the 555 timer in 2 modes:
  Astable
    With some calculations, we can determine the values of the capacitor and the 2 resistors (Ra and Rb) for astable operations.
  Monostable
    We can determine the value of the resistor and the capacitor with a simple formula for one-shot operations.
There are many other configurations and applications for this device.

## Slide 8: 555 Layout
Also available:
556 (two-555’s in one DIP package)
555 in a “metal can” configuration
1
2
3
4
8
7
6
5
Ground
Trigger
Output
Reset
Vcc
Discharge
Threshold
Control
1
2
3
4
5
6
7
8
Ground
Trigger
Output
Reset
Vcc
Discharge
Threshold
Control

## Slide 9: 555 timer- Pin Description
Pin | Name | Purpose
1 | GND | Ground, low level (0 V)
2 | TRIG | OUT rises, and interval starts, when this input falls below 1/3 VCC.
3 | OUT | This output is driven to approximately 1.7V below +VCC or GND.
4 | RESET | A timing interval may be reset by driving this input to GND, but the timing does not begin again until RESET rises above approximately 0.7 volts. Overrides TRIG which overrides THR.
5 | CTRL | "Control" access to the internal voltage divider (by default, 2/3 VCC).
6 | THR | The interval ends when the voltage at THR is greater than at CTRL.
7 | DIS | Open collector output; may discharge a capacitor between intervals. In phase with output.
8 | V+, VCC | Positive supply voltage is usually between 3 and 15 V.

## Slide 10: 555 Timer
Description:
Contains 25 transistors, 2 diodes and 16 resistors
Maximum operating voltage 16V
Maximum output current 200mA
If you input certain signals they will be processed / controlled in a certain manner and will produce a known output.
INPUT
PROCESS
OUTPUT
Best treated as a single component with required
input and output

## Slide 11: Oscillator Configuration
Externally, the 555 requires an RC circuit to create the time delays required for the time high and the time low.
Standard configuration requires
  common capacitor
  a resistor for the charge cycle
  a resistor for the discharge cycle

## Slide 12: General Configuration
Basic connections:
  Ground
  Vcc
    Note: some 555 timers may function at voltages other than 5 volts.
  Reset (active low)
  Output
1
2
3
4
8
7
6
5
Ground
Trigger
Output
Reset
Vcc
Discharge
Threshold
Control

## Slide 13: General Configuration
Specialized connections:
  Trigger
    monitors low voltage
  Threshold
    monitors high voltage
  Discharge
    path to ground, to discharge the capacitor
  Control
    specialized input
      filtering
      special applications
1
2
3
4
8
7
6
5
Ground
Trigger
Output
Reset
Vcc
Discharge
Threshold
Control

## Slide 15: Astable Configuration #1 (“Standard” Configuration)
1
2
3
4
8
7
6
5
Ground
Trigger
Output
Reset
Vcc
Discharge
Threshold
Control
Vcc
Ra
Rb
C
Vcc

## Slide 16: Astable
Filter Cap
0.01μF
Calculated
Values
Note: Duty Cycle must be > 50%

## Slide 17: Astable Configuration #1 (“Standard” Configuration)
Minimum duty cycle > 50%

## Slide 18: Calculations: Astable
TH
TL
Notes:
The value 0.693 is a factor associated with the
charge/discharge cycle of the 555 timer.
Duty Cycle must be > 50%
Time High, Time Low Set

## Slide 19: Sample Calculation
Design an oscillator with a frequency of 200Hz with a duty cycle of 78%.
  Determine Period (T):
  Determine TH and TL:
Time High, Time Low Set

## Slide 20: Sample Calculation
  Since there are 2 variables in the TL equation, select C:
  Determine RB by using the TL equation:
C=10μF
Time High, Time Low Set

## Slide 21: Sample Calculation
  Determine the value for RA:
Time High, Time Low Set

## Slide 22: Calculations: Astable
Notes:
The value 0.693 is a factor associated with the
charge/discharge cycle of the 555 timer.
Duty Cycle must be > 50%
Frequency, Duty Cycle Set

## Slide 23: Sample Design
Build an oscillator using a 555 timer with a frequency of 72kHz at 75% D.C. Use a 100F capacitor.
Frequency, Duty Cycle Set

## Slide 24: Design Solution
1- Determine the ratio of the resistors Ra and Rb:
2- Use the ratio in the frequency equation (substitution):
Frequency, Duty Cycle Set

## Slide 25: Design Solution
3- Solve for Rb:
4-Solve for Ra:
5-Use standard values (optional step):
Ra=100k
Rb=47k
Frequency, Duty Cycle Set

## Slide 26: Design Solution
6- Calculate actual frequency and DC:
Frequency, Duty Cycle Set

## Slide 27: 555 Timer as Monostable Multivibrator
Description:
In the standby state, FF holds transistor Q1 ON, thus clamping the external timing capacitor C to ground. The output remains at ground potential. i.e. Low.
As the trigger passes through VCC/3, the FF is set, i.e. Q bar=0, then the transistor Q1 OFF and the short circuit across the timing capacitor C is released. As Q bar is low , output goes HIGH.

## Slide 28: 555 Timer as Monostable Multivibrator
Fig (a): Timer in Monostable Operation with Functional Diagram
Fig (b): Output wave Form of Monostable

## Slide 29: 555 Timer as Monostable Multivibrator
Fig (a): Timer in Monostable Operation with Functional Diagram
Fig (b): Output wave Form of Monostable